## Slide 1
Lithium Ion Battery Safety
Non-Consumer Applications

## Slide 2: Non-consumer Lithium Ion Battery Safety
Where?
Custom UPS
Portable instrumentation
Detectors
Experiments
Research and Development
Who?
Technicians
Engineers
Scientists
Researchers
Operators

## Slide 3: Non-consumer Lithium Ion Battery Safety
Differences from consumer Li-ion
Increased capacity
Limited or absent safety measures
Not yet listed or tested by NRTL
Unusual or hostile environments

## Slide 4: Non-consumer Lithium Ion Battery Safety
Design
Safety circuits and cell monitoring are necessary to prevent thermal runaway
Separate positive and negative terminals and make touch safe, keyed connectors
Write operation and maintenance manual
Follow standards
  National
  DOE
  Site
Assembly
Physically protect batteries
Control temperatures
Do not solder to battery case
Label exterior of Li-ion devices

## Slide 5: Non-consumer Lithium Ion Battery Safety
Maintenance/Troubleshooting
Follow manufacturer recommendations
Split banks if possible to lower overall voltage, especially if system series potential exceeds 50 volts
Regularly inspect batteries
Replace all cells in system if one or more fail
Operation
Know signs of failure
Environmental limits
Follow procedures
Know Hazards
  Shock
  Burn
  Explosion
  Corrosive Chemicals

## Slide 6: Non-consumer Lithium Ion Battery Safety
Life cycle planning
Include capacity degradation when calculating required battery size
Design batteries in assemblies with integral safety and monitoring circuitry, and battery status communication to devices
Design devices for easy and safe battery assembly replacement
Design battery assemblies and devices for disassembly to facilitate re-use or recycling of components