## Slide 1: DOE-STD-5506-2021 (Revision of DOE-STD-5506-2007)
Robert C. Nelson, PhD
Office of Safety Management, CNS
ROLLOUT

## Slide 2: Background
Initially Issued in April 2007 revised August 2021
Unique Environmental Management (EM) standard that prescribes analytical assumptions and controls specific to the DOE Transuranic (TRU) Waste mission
Standard provides:
  Analytical assumptions and methods for hazard analysis and accident analysis
  Hazard controls to be used when developing TRU facility safety basis documents
  Supplements the applicable 10 CFR 830 Subpart B “safe harbor method” such as DOE-STD-3009, Preparation of Nonreactor Nuclear Facility Documented Safety Analysis for Documented Safety Analysis (DSA) development

## Slide 3: Why the Update?
Well past the sunset review period
Years of Lessons Learned and Feedback on Specific Topics in the Standard
TRU Waste Facility events (WIPP, ARP V)
Updates/linkages to other DOE standards (DOE-STD-3009-2014, DOE-STD-1104-2016, others)
Container tests
DNFSB Tech Report-43 (Deficiencies in DOE-STD-5506-2007) and DNFSB Tech Report-46 (Potential Energetic Chemical Reaction Events involving Transuranic Waste at Los Alamos National Laboratory

## Slide 4: Deleted Topics
  Section 4.2, Definition of Unmitigated Analysis
    Now explicitly covered in Section 3.2.2, Unmitigated Analysis in DOE-STD-3009-2014
    Section 5.2, Facility Worker Consequences
      Now discussed as part of the general discussion of Section 3.1.3, Hazard Evaluation in DOE-STD-3009-2014
    Section 5.3, Collocated Worker and Public Consequences
      Covered in Section 3, Hazard Analysis, Accident Analysis, and Hazard Control Selection, in DOE-STD-3009-2014
      Section 6.2, Risk Ranking and Control Selection Guidelines
        Now covered in Appendix A.4, Hazard Evaluation and Risk Ranking, in DOE-STD-3009-2014
Notes: “To ensure an informed and defensible qualitative evaluation, the determination of facility worker consequences should b e based on a combination of the following:
The magnitude, type, and form of radioactive and hazardous materials involved in a hazard scenario.
The type and magnitude of energy sources involved in a hazard scenario.
Characteristics of the hazard scenario such as duration and the location where it may occur )e.g., in unmanned areas such as tank vaults); and
The potential for a hazard to impact workers’ mobility or ability to react to hazardous conditions.
The facility worker’s mobility or ability to react to hazardous conditions should not be used as the sole or primary basis for determining facility worker impacts. As an example, an assumption that a worker within a building is unaffected by release from a building fire based on hazard recognition and timely evacuation would have to consider the location and characteristics of the fire relative to radioactive or hazardous material that may be affected by the fire (considering quantity, form, and dispersibility).
Facility worker consequences, due solely to a standard industrial hazard, do not need to be categorized in the hazard evaluation if screened out per Section 3.1.1. However, the evaluation of radiological or chemical hazards that result in a prompt death or serious injury should be assigned a high consequence per Table `. Examples of such hazards might include the generation of flammable/explosive hydrogen gas by electrolysis of uranium in water or a spill of sodium hydroxide used in radioactive waste processing.
The qualitative evaluation for the facility worker may be supported by scoping calculations, engineering judgment, and historical experience. This qualitative approach is used because quantitative estimates are sensitive to a variety of possible assumptions such as facility worker position, circumstance, and proximity to the point of release.”

## Slide 5: Deleted Topics (Continued)
Section 6.3, Clarification of What Challenges the Evaluation Guidelines.
  Now covered in Appendix A.10, Evaluation Guideline, in DOE-STD-3009-2014
  Section 7, Safety Basis Review and DOE Risk Acceptance
    Refer to DOE-STD-1104-2016, Review and Approval of Nuclear Facility Safety Basis and Safety Design Basis Documents
    Section 8, Verification of Safety Basis Implementation
      Refer to Appendix C, Implementation Verification Reviews (IVRs), in DOE G 423.1-1B, Implementation Guide for Use in Developing Technical Safety Requirements

## Slide 6: Implementation
Implementation of DOE-STD-5506-2021 is an interest item for the Defense Nuclear Facilities Safety Board
  DNFSB desired standard to a requirement or invoked standard
  EM and NNSA have resisted
  As part of DNFSB interaction EM and NNSA have requested field gap assessments.
  Gregory Sosson, Memorandum for Distribution, October 15, 2021, Implementation of Revised Department of Energy Standard 5506-2021, Preparation of Safety Basis Documents for Transuranic (TRU) Waste Facilities.
  Daniel Sigg, Memorandum for Distribution, October 12, 2021, Implementation of Revised Department of Energy Standard 5506-2021, Preparation of Safety Basis Documents for Transuranic (TRU) Waste Facilities.
  Gap Assessments Due February 28, 2022
  PSOs will make Implementation Decisions

## Slide 7: ARF / RF Comparison Table

## Slide 8: Damage Ratio Comparisons

## Slide 9: Future Training
Post Covid-19 Roll Out Plans
  Face to Face Instruction Sessions at Selected Sites Open for Attendance
    Savannah River
    Hanford
    Albuquerque/Los Alamos
    Per Request
    Projected 2-day Class
      Presented by Standard Writing Team SMEs
      Standard “Requirement” Use
      Updated fire analyses
      To include practical application and control selection exercises
        Training locations to be coordinated over next month taking into account local Covid Restrictions

## Slide 10: Gap Question/Answer Session
Session Scheduled next week to allow for questions/answers for members of writing team as a result of gap analysis exercise
Session Tuesday February 22, 2022
  12:55 PST
  13:55 MST
  14:55 CST
  15:55 EST

## Slide 11
Questions?