## Slide 1
EFCOG Safeguards and Security Working Group
NUCLEAR MATERIAL CONTROL & ACCOUNTABILITY
Office of Science (SC)
Implementation of DOE O 474.2A
Joseph Waggoner
Office of Science – Office of Safety and Security (SC-OSS)
April 17, 2024
Office of Safety and Security

## Slide 2
Office of Science (SC) Sites
Office of Safety and Security
SC-OSS Locations:
Lemont, IL;
Oak Ridge, TN;
Germantown, MD

## Slide 3
Brookhaven National Laboratory (BNL) / BHSO
Princeton Plasma Physics Laboratory (PPPL) / PSO
Thomas Jefferson National Accelerator Laboratory / TJNSO
Oak Ridge National Laboratory (ORNL) / OSO
Bldg. 3019 / OREM (EM) and OSO (SC)
Oak Ridge Institute of Science Education (ORISE) / OSO
Argonne National Laboratory (ANL) / ASO
Fermi National Accelerator Laboratory (FNAL) / FSO
Ames Laboratory / AMSO
Pacific Northwest National Laboratory (PNNL) / PNSO
Lawrence Berkely National Laboratory (LBNL / BSO
Stanford Linear Accelerator Laboratory (SLAC) / SLSO
Office of Safety and Security
Office of Science (SC) Sites

## Slide 4
Office of Safety and Security
SC MATERIAL BALANCE AREA (MBA) CATAGORIZATION
CAT IV MBAs
  9 out of 11 programs with exclusively CAT IV MBAs
CAT III MBAs
  1 site with three CAT III MBAs
  1 site with MBAs authorized for CAT III (within Limited Area), but remain CAT IV MBAs by quantity
CAT I MBA
  Facility on SC site in which the DOE O 470.4B S&S topical area oversight is split between EM (OREM) and SC (OSO), with MC&A under purview of OREM.
Office of Science (SC) Sites

## Slide 5
DOE O 474.2A IMPACTS
Office of Safety and Security
Level of Prescriptiveness (of CRD)
Table II, Table IX
Credible Substitution Materials
Termination of Safeguards process for inventory items / Pre-Disposition MBAs
Less than Accountable (LTA) Quantities of SNM
Rounding
Measurements – Confirmation Measurements
Key Measurement Points
Performance Assurance Program
Performance Testing of System Elements

## Slide 6
Office of Safety and Security
Level of Prescriptiveness (of CRD)
SC programs had already integrated Performance Metrics from DOE O 474.2 into their operations and MC&A Plans, which is where much of the detail in DOE O 474.2A CRD comes from.
Certain CRD clauses have caveats which specify ODFSA can approve alternative measures - MC&A Plans and flow down documents being revised accordingly.
    Extended inventory period for CAT III/CAT IV processing MBAs
    Quantity thresholds for measurements during physical inventory
‘Rightsized’ the SNM and OANM requirements:
CRD - CHAPTER II – OANM; 4 pages
CRD - CHAPTER I – SNM; 36 pages
DOE O 474.2A IMPACTS

## Slide 7
Office of Safety and Security
OANM (Table X)
DOE O 474.2A IMPACTS

## Slide 8
DOE O 474.2A IMPACTS
Office of Safety and Security
OANM (Table X)
Removal of certain material types from OANM list, increase in reportable unit quantity, and the less stringent Chapter 2 of the CRD provides considerable relief to SC programs ---
  Removal of Cf-252: no quarterly decay NMMSS transactions
  Raising the Deuterium (MT86) accountability from 0.1 kg to 100 kg: reduces frequency of reporting or D2 reporting all together.
  Accountable Depleted Uranium (MT10) being limited to DP materials: option to stop reporting DU inventory (as long as non-credible as substitution materials
  Manufactured items containing OANM no longer accountable: no transactions for DU-shielded casques used for radiological sources.
  OANM inventory tracked internally and reported annually – fewer transactions.

## Slide 9
Office of Safety and Security
Table II has not impacted MC&A posture at SC sites, however, it has alleviated confusion on material being controlled and accounted for as SNM, but being on the OANM list (in DOE O 474.2).
DOE O 474.2A IMPACTS

## Slide 10
Office of Safety and Security
Credible Substitution Materials
Due to the splitting of SNM and OANM requirements into separate chapters there is increased mention of credible substitution materials throughout the SNM Chapter 1.
Generally not applicable at SC sites due to –
  Prevalence of CAT IV MBAs
  Prevalence of ‘E’ attractiveness level materials
  Credible substitution scenarios not present in CAT III MBAs; basis for this assessment will be documented in MC&A Plans, as applicable.
CRD, Attachment 2, Chapter I, .d.(1), “…. When other nuclear materials are potentially credible substitution materials for Category I, Category II, and Category III (Attractiveness Levels B and C) SNM, are collocated with SNM, and there is a credible substitution scenario, the items must be under the same MC&A requirements as the SNM, with the exception of reporting credible substitution material to NMMSS, if otherwise not reportable.”
DOE O 474.2A IMPACTS

## Slide 11
Office of Safety and Security
Termination of Safeguards process for inventory items /
Pre-Disposition MBAs
Elimination of T.O.S. had significant impact on waste management operations for one SC site as previous T.O.S. approvals, once obtained, were advantageous since it removed constraints of MBA operations during packaging operations.
- Since these operations are conducted within an MBA, this change is manageable, and it will be a fundamental MC&A improvement for the site.
Elimination of TOS process, also means removal of EHSS-51 TOS consult, which will streamline future disposition campaigns. This change is certainly much more impactful for many NNSA sites.
SC sites do not currently see the benefit of Pre-Disposition MBAs to current operations.
DOE O 474.2A IMPACTS

## Slide 12
Office of Safety and Security
Less Than Accountable (LTA) Quantities of SNM
The main driver was to close a potential loophole of a research operation avoiding MC&A program applicability by keeping numerous individual ‘like’ items at non-reportable quantities (less than half of the NMMSS reporting unit).
It was not intended to force MBA-accountability on operations working with environmental-level or otherwise nominal sample quantities of SNM in which accumulation to a reportable quantity is not feasible.
One of the larger SC sites is planning initial and annual assessments of non-MBA operations that work with non-reportable quantities of accountable material types to make sure the technical basis precluding accumulation is established and remains.
Another (larger) SC site is planning to use chemical inventory tracking to identify total quantity of accountable material types in non-MBA operations (as part of initial technical basis assessment) and then set a conservative threshold for acquiring additional SNM quantities, that if to exceed, would require standing up an MBA.
DOE O 474.2A IMPACTS
Notes: Less Than Accountable (LTA) quantities of SNM.
(a) If the less than accountable quantities of SNM are containerized or put in a single shipment that exceeds an accountable quantity, then the total combined quantity must be within the boundaries of a material balance area (MBA) and be included on the facility’s nuclear material inventory.
(b) If similar less than accountable items within a location, such as an identified room or building, can cumulatively become an accountable quantity of SNM then an MC&A program must be established. Sites that possess LTA quantities of SNM must document the technical basis of how this requirement is met in their MC&A plan, if applicable, or alternate document approved by the ODFSA.

## Slide 13
Office of Safety and Security
Rounding
CRD, Attachment 2, Chapter I, .d.(5) and Chapter II, 1.b.(3).
(5) Rounding (Proposed Administrative change, “Rounding for NMMSS Reporting”, instead of “Rounding”)
SC has concurred with this proposed change.
Revision to MC&A Technical Standard, DOE-STD-1194-2019, will provide additional clarification regarding the need to sum full-precision inventory values BEFORE rounding.
For future reference when substantive changes are made in the next revision – it may add benefit to expand on the term ‘general calculations’ in the NOTE (below) from the ‘Rounding’ section [CRD, Attachment 2, Chapter I, .d.(5) and Chapter II, 1.b.(3)]
NOTE: When performing general calculations, do the calculation first before rounding. For software development purposes, sites or facilities may use more significant digits than provided in the tables.
DOE O 474.2A IMPACTS
Notes: Both element and isotope weights are reported if they round to are portable unit. In cases where the element is a reportable unit, but the isotope is not a reportable unit, the material is still to be reported, but for the isotope, enter 0 (zero). See Table III for Rounding, below.
(b) Quantities reported as shown in Table III for Rounding, below with fractions of one-half or greater of a reporting unit are rounded upwards and fractions of less than one-half of a reporting unit are reported as the number zero (0). Any item that contains nuclear material that rounds to a reportable unit for that nuclear material is accountable.
NOTE: When performing general calculations, do the calculation first before rounding. For software development purposes, sites or facilities may use more significant digits than provided in the tables.

## Slide 14
Office of Safety and Security
Measurements – Confirmation Measurements
CRD Chapter 1 (SNM) has additional detail regarding baseline measurement programs requirements that requires further consideration.
  Confirmation measurements – Several SC sites are in the process of qualifying gamma-spectroscopy methods to measure a characteristic of SNM during transfer checks and physical inventory, and to address anomalous conditions.
      Procuring traceable calibration and check standards
      Drafting or revising existing operating procedures
      Drafting qualification plans
      Developing and conducting analyst training and qualification
  SC sites that do not currently perform SNM measurements during physical inventory are considering ODFSA-approved threshold quantities for performing such measurements.
DOE O 474.2A IMPACTS
Notes: CRD, Attachment 2, Chapter I, 4.b.,
Program. All facilities possessing SNM must implement measurement and measurement control programs. Measurement programs used to determine Category III or IV inventories of SNM must address the topics set forth in paragraphs 4.c. through 4.f. below, but the specific measurement and measurement control requirements are to be approved by the ODFSA.
CRD, Attachment 2, Chapter I, 4.d.,
Measurement Methods. Each facility must develop, document, and maintain measurement methods for all SNM in inventory, excluding SNM not amenable to measurement.

## Slide 15
Office of Safety and Security
Key Measurement Points
CRD Chapter 1 (SNM) has additional detail regarding key measurement points.
SC sites need to address this concept with better clarity in the MC&A Plans and flow down documents, such as MBA procedures
  Sites were performing measurements that effectively supported accountability in most cases, but didn’t have KMPs defined.
  SC, NNSA, and EM counterparts may consider comparing notes on key measurement points for operations in CAT III and CAT IV processing MBAs to see if there are commonalities on implementation challenges.
CRD, Attachment 2, Chapter I, 4.b.(3);
Key Measurement points must be established and documented.
Key Measurement Point. A location where nuclear material appears in such a form that it may be measured to determine material flow or inventory. This includes: 1) inputs and outputs for material balances areas, 2) measured discards, 3) locations in the process where accountability values are determined, and 4) holdup locations.
DOE O 474.2A IMPACTS
Notes: Key Measurement Point. A location where nuclear material appears in such a form that it may be measured to determine material flow or inventory. This includes: 1) inputs and outputs for material balances areas, 2) measured discards, 3) locations in the process where accountability values are determined, and 4) holdup locations.
CRD, Attachment 2, Chapter I, 2.a(2)(d).,
Utilizes MBAs as the basis of the accounting structure with key measurement points established to
localize and identify IDs.
CRD, Attachment 2, Chapter I, 4.b.(3);
Key Measurement points must be established and documented.
Key Measurement Point. A location where nuclear material appears in such a form that it may be measured to determine material flow or inventory. This includes: 1) inputs and outputs for material balances areas, 2) measured discards, 3) locations in the process where accountability values are determined, and 4) holdup locations.

## Slide 16
Office of Safety and Security
Performance Assurance Program
SC-OSS comments on PAP sections of MC&A Plan revisions focused on whether all components were covered:
    Defined System Elements
    Evaluation of System Effectiveness
    Conduct of Internal Review and Assessments
    Performance Testing of System Elements
In general, each of these components were addressed in the plans, but often with different terminology, or each of the components were located in different parts of the Plan.
Each of the PAP components were revised to have more complete descriptions of the system elements, assessment methods, and performance tests.
DOE O 474.2A IMPACTS

## Slide 17
Office of Safety and Security
Performance Testing of System Elements
SC sites have made extensive progress in defining system elements that require performance testing and describing the PT program in their MC&A Plans.
However, for PT requirements from the CRD, Attachment 2, Chapter I, 1.e.(4).(a)-(f), compliance with the following is often incomplete.
  (f) Performance test plans must include the system elements tested, type of test (operability or effectiveness), test description/scenario, and clear pass/fail criteria.
  (g) The results of each test must be documented in accordance with DOE O 470.4, current version.
  For the smaller sites, performance tests and self-assessment activities tend to resemble each other, but with the self-assessments being fairly comprehensive and the credited PT’s lacking certain criteria – sites are drafting revised PT forms that have fields for all criteria.
DOE O 474.2A IMPACTS
Notes: Performance Testing. Each facility must establish and implement a documented performance testing program per DOE 470.4B, Safeguards and Security Program, to verify MC&A system elements are functioning as intended.
(a)Each facility must identify MC&A system elements which correspond to those components of the MC&A system that provide the greatest effectiveness against theft and diversion. These elements for testing must be used in the determination of the overall MC&A system effectiveness as applicable.
(b)MC&A system elements that must be performance tested are defined in the MC&A Plan.
(c)Each site/facility must define MC&A programmatic Essential Elements in accordance with DOE Performance Assurance Program policy.
(d)The MC&A Plan must document the MC&A performance testing program.
(e)The MC&A performance testing program must include establishing testing frequency for each system element.
(f)Performance test plans must include the system elements tested, type of test (operability or effectiveness), test description/scenario, and clear pass/fail criteria.
(g)The results of each test must be documented in accordance with DOE O 470.4, current version.
(h)Category I and II SNM sites must execute an integrated Safeguards and Security performance test utilizing a scenario which includes MC&A, Protective Force, and Physical Security System elements at least once every 12 months.

## Slide 18
Office of Safety and Security

## Slide 19
Office of Safety and Security
Joseph Waggoner
Physical Scientist
U.S. Department of Energy
Office of Science, Office of Safety and Security (SC-OSS)
Office: (630) 252-9711
MS Teams: (630) 884-9978
Joseph.waggoner@science.doe.gov

## Slide 20
Office of Safety and Security

## Slide 21
Office of Safety and Security

## Slide 22
Office of Safety and Security
TABLE I - SNM
TABLE I - SNM

## Slide 23
Office of Safety and Security
TABLE II - Ctrl &Acct as SNM

## Slide 24
Office of Safety and Security
TABLE III - ROUNDING

## Slide 25
TABLE IV - Graded Approach –
Graded Safeguards Table (GST)
Office of Safety and Security
Notes: Also available - DOE CUI Category List, CUI Labeling Training sessions, CUI Marking handbook

## Slide 26
Office of Safety and Security
TABLE V - EFFECTIVE QTY

## Slide 27
Office of Safety and Security
TABLE VI – Shipper/Receiver Meas

## Slide 28
Office of Safety and Security
TABLE VII – Physical Inventory Per

## Slide 29
Office of Safety and Security
TABLE VIII – Inv Periods/Alt Measures

## Slide 30
Office of Safety and Security
TABLE IX – Sampling/Phys Inv

## Slide 31
Office of Safety and Security
TABLE X – OANM

## Slide 32
Office of Safety and Security
TABLE XI – ROUNDING

## Slide 33
Office of Safety and Security

## Slide 34
Office of Safety and Security