## Slide 1
Subcontractor Electrical Safety Management (SESM) Working Group
Electrical Contact Release Training
WSH/ES-16-06
Notes: This course is intended to help Operations and Maintenance (O&M) Contractors for the U. S. Department of Energy meet the requirement in the 2015 edition of NFPA 70E, Article 110.2(C)(1) to provide annual Contact Release training to employees that require that training per Article 110.2(A).
This course includes additional information to place Contact Release within the larger context of preparing for and responding to unexpected conditions and events.
The intended audience is Qualified Electrical Workers and First Responders. Certain terms and concepts used in this course may not be familiar to other workers and are not further explained here.
Course organization:
  Preparation for performing work with electrical hazards
  Immediate actions preparatory to Contact Release
  Circumstances in which Contact Release should not be performed
  Indications of contact with energized electrical components
  Common methods of Contact Release
  Follow-up actions after Contact Release is performed

## Slide 2
Preparing for work with electrical hazards
  Review work-site specific hazards, identify de-energization points, and discuss potential rescue scenarios and techniques. Ensure work crew size and training is adequate to respond to emergent conditions.
  Use correct shock and arc flash PPE. Use non-conductive ladders, platforms, and barriers, insulated tools, and insulating mats and blankets.
  Designate the person who will direct rescue efforts
  Provide at the worksite, or identify at a location nearby:
    Means for contacting First Responders:
      Landline or cellular telephones (verify reliable reception)
      Continuously monitored jobsite two-way radios
      Fire alarm manual pull stations
    Automated Electric Defibrillator (AED)
    Adequately rated and inspected rescue hooks, if appropriate
Contact Release Training
Notes: Sustained contact with energized components is an improbable event – most likely resulting from:
An unidentified or unanticipated hazard
Equipment failure
Inadequate work planning
Human Error

## Slide 3: Contact Release Training
Response Actions
Notify First Responders first – get more help on the way
  No matter what else happens, the victim will need prompt medical attention
  Other work team members or even a passerby can do this
Remember: the safest method of contact release is to turn off the power
  If there’s an obvious and safe way to turn off the source, DO IT!
  Do not consider other contact release methods until options to quickly isolate the source have been exhausted

## Slide 4
Release the Victim
Contact Release is a high-risk activity – for the rescuer!
  Many well-intentioned rescuers have become an additional casualty instead
Perform a real-time risk assessment
  Assume the victim is still energized when assessing the incident
  Do not assume the hazards you expected are the only ones present
  Assess the situation
    Identify energized components which the victim could be contacting, or that the rescuer could contact
    Observe the victim for signs they are still receiving a shock
Contact Release Training
Notes: Potential signs of victim receiving electric shock:
  Victim stops talking or won’t respond to your questions, or makes unintelligible sounds
  Victim is flailing wildly, slumped and motionless, in an awkward or rigid position, or only capable of slow, deliberate movements.
  Facial expression may be a grimace, jaw may be clenched
  A victim on a ladder or work platform may attempt to kick their support away

## Slide 5: Contact Release Training
If unable to isolate the power, determine if other contact release methods are advisable
Time is critical for the victim
  Chances for survival decrease every minute a person is in ventricular fibrillation or respiratory paralysis.
  National average for EMS response is over 15 minutes
  Prompt rescue is vital for survival and minimizing brain injury
Notes: Contact Release should not be attempted:
  In a confined space
    Self-rescue if in the confined space, otherwise do not enter
  In fires, or near releases of flammable, toxic, or radiological materials
    Rescues must be performed by trained and experienced personnel with appropriate protection
  In rain, snow, or other wet conditions
  On scaffolds
    The multiple risks to the rescuer are simply too great
  Near downed overhead electric lines, on utility poles, in underground cable vaults, and in substation yards or buildings
    Even trained emergency responders do not engage this type of situation until the utility has shut down the source

## Slide 6: Contact Release Training
Some Accepted Rescue Techniques when isolating the power is not an option
  The rescuer cannot forget that they are about to contact a potentially energized victim and must protect themselves.
    Designated rescuers should don PPE appropriate for the hazard – preferably before the hazardous work starts
    Rescuers must maintain a firm and stable posture
    Use a rescue hook to remove the worker from the source
    Push or pry the worker away with a DRY board or wooden broom handle.
        Note: New lumber delivered to a construction site is wet and is not safe for rescue

## Slide 7: Contact Release Training
  Higher Risk Rescue Techniques
  Use voltage-rated gloves to grab or push the victim free
  Use a dry belt or rope to grab or pull the victim from the source
  Using insulated tools or gloves, pull the victim off a ladder or platform
  If there is sufficient space, as a last resort a flying football tackle can be used to propel the victim and rescuer away from the source

## Slide 8: Contact Release Training
Next Steps
  Tend to the victim
    Move victim to a safe place
    Initiate CPR, use AED if necessary
    Perform first aid for other injuries
  Secure the area
    This can be as simple as informing others that there’s still an energized hazard at the scene
    Be the “expert” at the scene. Be prepared to communicate the situation, hazards, and victim status to First Responders